____________________________________________________

    Chapter 1
____________________________________________________

L.10 You should start with a more general context, i.e. on High-Luminosity LHC program (one sentence).
        Then down to ITk, briefly describing the overall design and finally the strip detector.
        That's the first paragraph of your abstract.
        You should add right after what we mean by a petal (look up Yu-Heng's report).

L.12 CO2 => CO outside of math type
L.13 This thermal cycle result (lack of thermal memory) is a "by-product" of our tests (we had to go down in temperatures so we recorded all the intermediary steps)
        But it is not the most important things we wanted to measure at the first place, that is to say the temperature of the silicon sensors of a powered + cooled down petal.
        So announcing this result gives way too much importance. On top of it, we did only one thermal cycles. Typical dedicated measurements of thermal memory involve ~30 cycles or more.
        I would quote instead the lowest temperatures we reached on the sensors.

L.15 remove "also"
L.16 "In addition, a thermographic correction". This is the main goal of the report and how measurements are made. So it should not be a supplement but it's the core of things
        This should be mentioned in the abstract (not too detailed such as quoting the black tape method, but stating that we correct the raw camera output).
L.18 "would eliminate the necesity of covering the petal surface with high emissivity black tape." => if you write this in the abstract, you need to define it more
        I would rather stay general with something like "this report details a method used to calibrate the temperature provided by the infra-red camera".

L.19 The viewing angle is rather to be seen as a preliminary study to understand more our system.
        If you really want to put it in the abstract (I would not), it should go before the final result.

First impression on the Table of Content:

        I would merge chapters 3 and 4.
        At least chapter 3 is not "Analysis", but "measurements".

L.58 "it’s however the most important component on the detector sensors." => component is usually used for electronics. Here we are dealing with a block of silicon.
        Suggestion: "it is what the sensors are made of"
L.60 sensor’s response => sensor’s thermal response.
        The connection between infrared thermography and FEA can be improved. You already justified the relevance of contact-free thermal measurements above.
        So you could say "Moreover, simulations using FEA give the thermal response of the sensors... " You could start a new paragraph on FEA in your intro I think.

L.62 "this simulation model have to" => has or models?
L.63 thermo-mechanical: uniformize the spelling. FYI TDR uses the dash.
L.75 "subsequent sections is" => "subsequent sections, is"
L.77 analysis methods => measurement methods? are we analyzing yet or just taking data?
L.78 "results are presented accompanied by a small discussion." => [up to you] "results are presented and discussed"

L.83 "Infrared measuring devices" => I am not sure we can say that. I would say "Such devices..."
L.88 "to it which" => "to it, which"
L.89 you mention as first and unique caveat in this paragraph the path between object under study and camera.
        This plays very little role in our case. It's a secondary issue, I would say.
        With this last sentence of the paragraph we can conclude that in vacuum we have no problem at all and the camera will always say the truth.
        I understand it's difficult to mention stuff like emissivity etc, as it's only the intro.
        But you should rephrase that end of paragraph so that the reader does not believe that infrared in vacuum is calibration-free.

L.93 is the lower limit 0.7 or 0.8 micrometres?
L.97 There are different division schemes but all the time (wikipedia, Infrared book) I do not see any gaps nor overlaps. Not the case here.
        https://en.wikipedia.org/wiki/Infrared
        Ref 11: Byrnes, James (2009). Unexploded Ordnance Detection and Mitigation. Springer. pp. 21–22. ISBN 978-1-4020-9252-7.
        So please fix the boundaries
        Suggestion: 0.75 - 1.4 - 3 - 8 - 15
        (the 0.75 needs to be in the text to for consistency)
L.100 Far infrared?
L.109 Would it be better to write the equation without C1 and C2? They are defined with c, h, and k_B,
        so I would just write the equation without these constants first, or at least put the definition of these C1 and C2 somewhere
        for exp() use "e"

        Figure 1.1 is pixelized. Any better resolution somewhere?
        Figure 1.2, caption: ... we can see the molecule responsible of the absorption.

L.117 Google does not find reference 6:
        Selected critical applications for thermography: Convection in fluids, selective emitters and highly reflecting materials.
        Proceedings of the Infrared Camera Calibration Conference, vol. 6, (Las Vegas (NV), USA), pp. 161-173, oct 2015.
        Could you send it to me please? Thanks.
L.126 opaque => you should precise opaque in infrared radiation
L.130 Incorrect English. Rephrase and check with a native speaker.
L.136 tempeture => " and wavelength".
L.140 You are reversing cause&consequence. It's because of the definition of a black body, which is an idealization, that any other object will emit less.
        So reverse the two proposition of that sentence to end with eps is between 0 and 1.
L.141 I do not see the emissivity constant on the graph.(because it is the ratio btw blackbody and greybody what remains constant… will be seen when I add the other plot beside it)
L.141 grey body => no entry on Wikipedia nor the Infrared book. "Gray" exists. Correct and add the other image of the book.
 https://www.spiedigitallibrary.org/ContentImages/Proceedings/10452/104522C/FigureImages/00022_PSISDG10452_104522C_page_2_2.jpg
 (find a vectorial version if possible as this is too pixelized)
Figure 1.4: we can't see here that the black body yields maximum radiance. With respect to the others yes it's greater in value but who tells us it is a max?
        Would remove this. Will be clearer once you add the other graph with eps_b at 1 for all lambda.
L.152 so-called
L.154 temperatures (temperature is correct)
L.161 "will have to absorb" => "will absorb"
L.165 "This law also applies to non-blackbodies" => as an approximation (no, it applies to all surfaces but the blackbody is a particular case…. easier to explain….this is merely an expression of the 2nd law of thermodinamics)
L.177 "perceives" => rather "displays" (hmmm...I dont know, display is not the word I’m looking for here… it’s more like in the other direction: receives, perceives, feels… “displays goes in the opposite direction”)
        these factors
L.178 would be cool to classify this as they did in the book: intrinsic object properties (material, surface, geometry) and other paramethers (viewing angle, wavelength, ambiant)
L.179 capital letters not necessary
L.184 these factors
L.192 These other contributions
L.193 on the target surface
Fig 1.6:"(D) external source radiation transmitted through the target." => external source of radiation
Eq 1.11 write it first generally and then say we neglect the transmissive part and write the updated equation.
        Otherwise the equation, taken out of its context, is wrong, and we don't want that.
L.207 would remove "petal" parenthesis as you haven't defined the concept and it would be too long here. You have Chapter 2 for that.
L.214 where (no capital letter)
L.215 I would remove the footnote as it is not necessary + the current chapter is not about the setup (I think it’s important to “justify” this here even though we are not talking about the experimental setup just yet...)
L.218 same as above 'where'
L.221 reference needed here. Also I am surprised I do not find much with a Google search and the book has p.118 one four-line paragraph on it.
        I think this efficiency is already accounted for. I would be happy to read your reference + exchange with Peter (for me it’s the only explanation why we see that constant difference btween what the IR camera reports and the theoretical calculations… in any case it’s obvious that we are not accounting for something (whatever it might be) constant and independent of the surface type and temperature, as the study with the aluminum bucket showed...)
L.229 can we average? what are the physics justification? (yes we can, and we must, otherwise we hit the wall here because there is no way to know the lambda dependence of emissivity, we can use the IMV theorem here since, as I point out in the text, both R and epsilon are slow varying functions of lambda)
L.236 just refer "see study ..." and don't detail too much in that theoretical introduction
L.239 I would start a paragraph entirely dedicated to the angular dependence
L.241 capital letter blackbody + remove extra space
L.242 radiance has 2 occurances, one p.6 and here p.9 but it is not defined. Caution: irradiance != radiance. See Infrared book or https://goo.gl/J588aH
L.247 it is not an approximation, it's the law: https://en.wikipedia.org/wiki/Lambert%27s_cosine_law (no it’s not… this cosine law is for the spectral “intensity” which is the integral of the radiance over the solid angles. The intensity follows a perfect cosine law only for blackbody sources or perfect diffusely scattering surfaces which integrate nicely and we only have left the geometrical cosine dependence coming from the projection of the unitary area in the plane perpendicular to the direction of emission… I have refrased the last paragraph to make that a bit more clear...in agreement with the next point, which is the correct one)
L.248 the necessity of the measurement came from other experimental factors we cannot quantitatively estimate (property of the surface, etc)
        and the geometry of the setup having different angles along the petal's length. You need to rephrase here.

____________________________________________________

    Chapter 2
____________________________________________________

L.251 reminder of "thermo-mechanical" to stay coherent in your report + with respect to TDR
L.252 the reader may better understand if you do not start by quoting petal but rather
        zoom in as you nicely did afterwards, with key words end-cap => discs => support structures.
        Then you can state they are called "petals"
L.254 remove "structural" and be more general instead of "CO2 cooling" => provides the electronics and cooling services.
L.255 a petal has 9 sensors, remove parentheses for silicon
L.256 ATLAS Phase II (reverse order)
L.257 add mostly because R0 is not. "parts" => replace by "modules" and you can add it has "blank silicon"
L.261 the employment of non-contact ... very difficult (typo non-contact + order of words)
L.263 the metallic finish is at the back. Writing this may confuse the reader as the metallic part is reflective...
        sugested workaround: you can summarize the whole by being general on the different waffers
L.264 would remove this sentence (it diminishes your work for no reason!)
Figure 2.1 the global support structures are shown on the left (you can add some petals are drawn). Replace "design" by schematics
L.265 don't mix modules and rings
L.275 "the prototype counts with real cores" => what is "real" in this case? say "built with the real materials" (with respect to preliminary petal designs)
Figure 2.2 used for
L.280 support tends to refer to the end-cap structure. "vertically inserted in a custom rail system"
L.284: "on the one hand ... on the other hand" = used when you are comparing two different facts or two opposite ways of thinking about a situation
        say "first... second" or "moreover"
L.292 angle of incidence
L.316 infrared opaque
L.323 there is no interference pattern here. Just "blurred the thermogram"
L.326 more precisely: that a petal thermo-mechanical prototype was cooled down using by-phase CO2.
L.330 four? (one per ring + 1 eos ) x 2 sides
L.332 write: (25 W for one side's powerboard plus 3 W for the Eos)
L.334 remove the setpoint difference as it is related to TRACI operations.
        Moreover this was not safe, as we had no way to control this except tweaking manually
        I would remove it, as it is too close to the unknown zone on how to use TRACI properly.
L.346 maintained by a piece of high emissivity black tape

____________________________________________________

    Chapter 3
____________________________________________________

-----------------------------------------------------------------

Main comment:

Your report is structured with the different measurements in this chapter + the results in Chapter 4.
That could work, but in your case I think your report would be much better to have

Chapter 3: Preliminary Measurements
Chapter 4: Calibrated Thermograms

First it would flow better because you will have the results following right after the description of each measurement.
Second it is crucial to end your report with the main, most relevant results. Other satellite measurement contributing to it should be detailed beforehand.

-----------------------------------------------------------------

L.352 ...surface, it .. (add comma)
L.359 add internal control ... and *the* distance
L.360 the reader doesn't know (yet!) that all part of the alu foil is a region of interest.
        you can add: "..., i.e. an area of the aluminium foil" or something like that
L.364 remove s at distance
L.365 "The emissivity and distances settings of 1.00 and 0 m respectively are just telling the camera that record everything
        without applying any further correction" => awkward phrasing
        => The camera emissivity is set to 1.00 and the distance to 0 so that the IR camera software does not apply any further correction.
L.370 add "the" for emissivity and apparent temperature
L.378 suggestion: split this long sentence in two: "The surface was coated with..." + water temperature goes down
L.380 the emissivity
        I am not sure I understand this. What do you want to say here?
        moreover you say L.445 "Let’s now discuss another method, known as the “baseline image” method." I am confused on the methods here. (There are, among others, two methods that I discuss in the report: The “black tape” method, which is the one we used for all the results... and the “baseline image” method, which we do not use but, I think it’s worth discussing since it’s a non-contact offline method that in principle eliminates the necessity of covering the Si with BT. That would be ideal right? However, the difficulty of this method is precisely in how to get the baseline image correctly. Here, as I discuss in the report are two main problems: 1) the Si surface might be quite transmissive. And 2) Ambient temperature is not recommendable as the baseline image temperature.)
L.396 remove "known emissivity coating" (nope… this I can’t remove because was in fact what we did!… Please note that at this point the description of the method (relative methos) is kept general, therefore it doesn’t matter which alternative temp. measuring method we use (thermocouples or black tape…). Only later I state that we went for the “coating” one since attaching thermocouples was complicated and dangerous. We did used thermocouples but as a way to double check the BT in some areas)
L.398 "necessary measurement parameters in the IR camera software" => which ones?
L.403 repeating won't decrease the uncertainty due to the resolution of the camera
        I would go for a safer phrasing saying that we can to average out the "flickering effect" of the thermograms (again, at this point this is a general procedure, in fact it is extracted from references 11 and 12, I can’t change what they said… )
L.405 on the silicon surface
L.414 Let's
Eq.3.2 not sure it is okay with the indices. Should be Si and not TB. Or I didn't get the reasoning here.
        Edit: ok never mind I think I get it.
        However it is confusing in the way it is introduced.
        We can talk about it on how to explain best but as we are looking for T_Si, perhaps it's better to start from there. (You are right, this needs to be rephrased in a better way… will do)
L.422 the small trick seems to be an equation rearrangement but it is rather motivated by the physics.
        I would strongly recommand to rephrase.
L.432 the black tape used for this setup has an emissivity...
L.434 till line 436: sentence not grammatically correct and too long. Split in two and put for the second the concept
        of thermodynamical equilibrium
L.438 trustable => calibrated, or adjusted
L.441 Additionally,... => I would add this sentence on Si markers right after the one on BT markers
L.445 "If" => Let's
L.450 why italic?
L.458 "from one to the other" => inbetween
L.464 put the footnote exponant on the "impossible"
L.467 not sure viewing angle is the proper term. Suggesting "Influence of radiation emission angle"
L.468 "viewing angle of the camera with respect to the normal to the petal" => angle of incidence of the petal's emitted radiation
L.469 studies are not angular :) just put "a dedicated study" or "a study"
L.470 "Petal. and" => please correct + rephrase "viewing angle"
L.475 typo "ro's" => rod

____________________________________________________

    Chapter 4
____________________________________________________

L.478 change title, Ramp up and down in temperature
        => see comment line 490 to properly introduce this section
L.479 CO2 not italic
L.482 PT100, put before "resistance thermometer"
L.488 it would be nice if you have time to split what is purely TRACI from the rest
L.489 recorded at each step following...
L.490 The results => caution, these are 'nearby products'. It is a result but not what we are directly looking for.
        Just because we end up storing each point we get a thermal cycle but it's not a real one. Usually 30 cycles can tell something on sensor memory.
        You should mention that. Calling ramping down and up of the temperature.
        Also I would strongly recommend to not refer to the 2 and 9, that's internal data for us.
        In a report, it will read better if you use unpolished (back side) and polished (front side) [replace all occurences of 'cycle 2' and 'cycle 9']
L.502 "that we wanted to perform was" => that was performed is
L.509 miss-contact => bad contact
L.512 setpoint => temperature setpoint
        R3(border) => space missing
L.513 "With this results we also see that the tendency of the sensors is to not having memory
        (i.e. they are not damaged) after the thermal cycles, which was one of the main concerns that motivated the thermal tests."
        => to remove, as explained above
        You can briefly mention "The ramp down and ramp up slopes look mostly symmetrical, with the latter slightly stayin towards lower temperature values
        (within the IR camera uncertainties)
P.23 if you can, crop the title of the plots
Fig 4.1 the dots represents *the* setpoints where the petal's electronics was not powered
        for the parenthesis on CO2 [not italic] add: ... , given by the TRACI system)
        I think "represent(s) temperature values read by" ... flows better, please check with a native
L.517 it's confusing in the way it is phrased, although the science is right.
        stay general first: In order to compare the measured temperature values of the silicon sensors with the ones given by the FEA simulations,
        the black tape method was applied using IR camera readings from the black tape strips.
L.518 lowest point thermogram => thermogram at the lowest temperature achieved
L.519 red squares are => correspond / delimit
L.520 "between the marker points corresponding to the black tape measurements" => inbetween each marker
L.521 space missing before parenthesis + isotherm map of the sensor
L.527 "is very hard to model" => add and is not accounted for in the FEA simulations. I would rephrase "the very complicated" (remove absorption, we include that. Just convection)
        => the thermal convection or heat transfer by convection
L.530 "figure out a large area where there is no experimental point" => to connect to distant measurement zones
Fig 4.2 "linear interpolation isotherms for the sensors" => Isotherm contours are drawn using a linear interpolation between each markers.
        Note (most important): your report should end with these plots. Before are all preliminary / satellite studies contributing to these nice results.
        + FEA plots SHOULD be next to the infrared measurements. In an A4 format landscape for instance you can fit these 4 plots.
        Or better 2 big IR+FEA plots on one full page for one side, another entire page for the other side

L.539 at the start of this session, the reader can legitimally ask what this non-invasive technique hasn't been done before (see above)
        once you reshuffle the chapters & sections, it will flow better (here it repeats itself)
L.549 "as this variant is more like a black box to us," => fine but you can also say "as the calculations not known in IRBIS proprietary software"
L.551 opaque => infrared opaque + well away => significantly different than the ambient
L.554 "profile plot" add: (azimuthal projection) + temperature setpoint
L.557 "It is appreciable the difference between the temperature values of black tape and silicon markers." => sentence grammatically wrong & I don't get it sorry
L.558 for the high apparent temperature in Si you can simply say that is collects all reflections
Fig 4.4. this remains still very qualitative and it would be crucial to know the scale. Has this be saved in IRBIS?
L.571 the petal at room temperature without cooling nor electronics powered on.
L.578 plays
Fig.4.8 it's not okay to draw a horizontal line for all marker number (i.e. position) for the thermocouple value as you haven't measured it for each point.
        you assume it's flat. It should be clear in your plot that the blue series is only taken at marker 24. Either modify the plot or rephrase the caption.
        add the uncertainty for the PT100 blue series

_____________________________________

 CONCLUSION
_____________________________________
L.587 remove s
L.588 no thermal cycle => put 'thermal behavior' + thermo-mechanical petal prototype of the ITk strip sensor for ATLAS Phase II upgrade are presented.
        (it's heavy I know but conclusion needs to get all keywords)
L.590 would not quote inlet pipe but TRACI data
L.595 "of the PT100s are observed for a couple of sensors." => of some PT100 sensors were observed.
L.596 see remark above on that
L.604 careful: it can be highly reflective in the visible range but not necessarily in the IR one. Have you checked that?
L.606 for a shorter conclusion, I would remove the paragraph on the response scale factor
L.611 instead, put viewing angle before and end with an outlook. "Further investigations...."